## Slide 1: JVET-AJ0226 AHG12/ AHG10 : Using CABAC cost for MTT split modes selection
Waqas Ahmad, Per Wennersten, Kenneth Andersson
Ericsson

## Slide 2: Background
Several proposals have been presented to reduce the encoding runtime for ECM.
  Such as JVET-AA0098, JVET-AD0197 , JVET –AD0128, JVET-AD0105, and JVET-AF0111.
In JVET-AF0111, a condition is applied on the no-split cost of 64x64 luma CUs. If the no-split cost is greater than a threshold, MTT splitting will not be evaluated. The threshold is set based on QP value as follows:
This contribution presents a modification to this MTT split modes early termination method (JVET-AF0111) for ECM & VTM.

## Slide 3
We proposed to modify the threshold defined in JVET-AF0111 as follows:
Here,
T represents the threshold value.
represents value of a slice QP.
represents value of a base QP.
represents the strength applied to the CABAC cost. It is set to 4, 2, 1, 0.5 for QP 22, 27, 32, 37.
represents the CABAC cost to code the MTT split mode flag.
Proposal
No_split
Split_QT
Split_BTH
Split_BTV
Split_TTH
Split_TTV

## Slide 4
QP-22 runtimes are 90.7%, 86.1% and 86.6% for AI, RA and LDB configurations.
Results
Test 1: Condition applied to 64x64 and 32x32 luma CUs.
 | BD-rate Over ECM-14.0 |  |  |  |  | 
 | Y | U | V | EncT | EncT-QP22 | DecT
 | All Intra Main 10 |  |  |  |  | 
Class A1 | 0.01% | 0.00% | 0.04% | 98.0% | 94.2% | 100.7%
Class A2 | 0.02% | -0.01% | 0.01% | 97.3% | 90.3% | 99.9%
Class B | 0.01% | 0.05% | 0.03% | 97.9% | 93.1% | 99.4%
Class C | 0.01% | 0.05% | 0.08% | 94.1% | 83.2% | 99.9%
Class E | 0.00% | 0.00% | 0.00% | 98.4% | 94.3% | 99.6%
Overall | 0.01% | 0.02% | 0.03% | 97.0% | 90.7% | 99.8%
Class D | 0.00% | 0.01% | 0.01% | 95.2% | 86.2% | 99.8%
Class F | 0.00% | -0.05% | -0.04% | 97.7% | 90.8% | 100.3%
Class TGM | 0.03% | 0.00% | 0.01% | 97.5% | 94.0% | 100.5%
 | Random Access Main 10 |  |  |  |  | 
Class A1 | 0.03% | 0.04% | 0.03% | 97.2% | 90.7% | 100.5%
Class A2 | 0.08% | 0.07% | -0.07% | 95.6% | 84.5% | 99.8%
Class B | 0.01% | 0.07% | 0.10% | 95.6% | 86.6% | 99.8%
Class C | 0.03% | 0.13% | 0.12% | 94.5% | 83.4% | 99.3%
Class E |  |  |  |  |  | 
Overall | 0.03% | 0.08% | 0.06% | 95.6% | 86.1% | 99.8%
Class D | 0.04% | 0.00% | -0.05% | 94.6% | 83.2% | 99.3%
Class F | 0.07% | 0.08% | 0.08% | 96.4% | 88.5% | 99.7%
Class TGM | 0.11% | 0.15% | 0.05% | 97.7% | 93.0% | 101.0%
 | Low delay B Main 10 |  |  |  |  | 
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.10% | 0.18% | -0.20% | 96.5% | 89.0% | 100.3%
Class C | 0.05% | 0.00% | 0.14% | 94.8% | 83.5% | 100.2%
Class E | 0.08% | -0.05% | -0.08% | 96.6% | 86.7% | 99.8%
Overall | 0.08% | 0.06% | -0.06% | 96.0% | 86.6% | 100.1%
Class D | 0.05% | 0.51% | 0.34% | 95.9% | 86.8% | 100.4%
Class F | 0.02% | -0.24% | 0.25% | 97.5% | 92.9% | 99.5%
Class TGM | 0.03% | 0.13% | 0.01% | 97.8% | 93.8% | 100.2%
 | BD-rate Over VTM23.4 |  |  |  |  | 
 | Y | U | V | EncT | EncT-QP22 | DecT
 | All Intra Main 10 |  |  |  |  | 
Class A1 | 0.01% | 0.01% | 0.01% | 98.5% | 94.0% | 99.4%
Class A2 | 0.01% | 0.02% | 0.03% | 97.3% | 90.7% | 99.7%
Class B | 0.01% | 0.02% | 0.03% | 97.7% | 92.5% | 99.6%
Class C | 0.01% | 0.03% | 0.02% | 93.9% | 82.7% | 100.2%
Class E | 0.00% | 0.01% | 0.00% | 98.4% | 95.0% | 100.0%
Overall | 0.01% | 0.02% | 0.02% | 97.0% | 90.6% | 99.8%
Class D | 0.01% | 0.05% | 0.04% | 94.8% | 84.9% | 100.5%
Class F | 0.00% | 0.00% | -0.04% | 97.4% | 91.3% | 99.1%
Class TGM |  |  |  |  |  | 
 | Random Access Main 10 |  |  |  |  | 
Class A1 | 0.05% | 0.04% | 0.01% | 95.4% | 86.2% | 100.3%
Class A2 | 0.10% | 0.05% | 0.07% | 92.8% | 78.1% | 99.8%
Class B | 0.05% | 0.13% | 0.06% | 94.7% | 83.8% | 99.3%
Class C | 0.05% | 0.10% | -0.01% | 94.1% | 83.9% | 100.3%
Class E |  |  |  |  |  | 
Overall | 0.06% | 0.09% | 0.04% | 94.3% | 83.1% | 99.9%
Class D | 0.06% | -0.04% | 0.09% | 95.3% | 86.7% | 100.6%
Class F | 0.07% | 0.11% | 0.06% | 96.5% | 89.8% | 100.7%
Class TGM |  |  |  |  |  | 
 | Low delay B Main 10 |  |  |  |  | 
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.08% | -0.14% | 0.42% | 93.6% | 82.4% | 100.1%
Class C | 0.16% | 0.01% | -0.17% | 93.4% | 83.7% | 99.4%
Class E | 0.13% | 0.18% | 0.26% | 95.9% | 86.0% | 100.4%
Overall | 0.12% | -0.01% | 0.18% | 94.1% | 83.7% | 99.9%
Class D | 0.03% | 0.33% | 0.29% | 94.8% | 84.8% | 100.5%
Class F | 0.05% | 0.28% | -0.10% | 95.7% | 88.8% | 99.1%
Class TGM |  |  |  |  |  | 
QP-22 runtimes are 90.6%, 83.1% and 83.7% for AI, RA and LDB configurations.

## Slide 5
QP-22 runtimes are 92.4% and 92.0% for RA and LDB configurations.
Results
Test 1: Condition applied to 64x64 luma CUs.
 | BD-rate Over ECM-14.0 |  |  |  |  | 
 | Y | U | V | EncT | EncT-QP22 | DecT
 | Random Access Main 10 |  |  |  |  | 
Class A1 | 0.02% | 0.03% | 0.01% | 98.0% | 93.2% | 99.7%
Class A2 | 0.06% | 0.05% | -0.07% | 97.1% | 89.7% | 99.9%
Class B | -0.01% | 0.00% | 0.06% | 97.1% | 91.1% | 100.1%
Class C | 0.02% | 0.02% | 0.16% | 98.2% | 95.4% | 100.2%
Class E |  |  |  |  |  | 
Overall | 0.02% | 0.02% | 0.05% | 97.6% | 92.4% | 100.0%
Class D | 0.01% | 0.14% | 0.02% | 99.1% | 97.3% | 100.8%
Class F | 0.02% | 0.01% | 0.00% | 98.4% | 95.5% | 99.6%
Class TGM | 0.01% | 0.07% | 0.00% | 99.4% | 99.1% | 100.4%
 | Low delay B Main 10 |  |  |  |  | 
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.08% | 0.00% | 0.01% | 97.4% | 91.9% | 100.6%
Class C | 0.04% | -0.02% | 0.21% | 98.5% | 95.6% | 100.1%
Class E | 0.05% | 0.03% | -0.03% | 97.0% | 87.7% | 100.0%
Overall | 0.06% | 0.00% | 0.07% | 97.7% | 92.0% | 100.3%
Class D | 0.02% | 0.77% | 0.37% | 99.3% | 98.7% | 99.2%
Class F | 0.10% | -0.26% | -0.15% | 98.9% | 97.4% | 99.4%
Class TGM | -0.04% | 0.11% | 0.10% | 99.2% | 99.0% | 98.9%
 | BD-rate Over VTM23.4 |  |  |  |  | 
 | Y | U | V | EncT | EncT-QP22 | DecT
 | Random Access Main 10 |  |  |  |  | 
Class A1 | 0.04% | 0.05% | 0.01% | 96.8% | 89.6% | 100.2%
Class A2 | 0.09% | 0.02% | 0.07% | 94.7% | 82.9% | 100.6%
Class B | 0.04% | 0.11% | 0.01% | 95.9% | 87.5% | 99.1%
Class C | 0.02% | -0.01% | 0.02% | 96.9% | 93.5% | 100.9%
Class E |  |  |  |  |  | 
Overall | 0.04% | 0.05% | 0.02% | 96.1% | 88.5% | 100.1%
Class D | 0.00% | -0.04% | 0.01% | 98.8% | 98.1% | 100.4%
Class F | 0.02% | 0.08% | 0.05% | 97.9% | 94.2% | 100.3%
Class TGM |  |  |  |  |  | 
 | Low delay B Main 10 |  |  |  |  | 
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.07% | -0.06% | 0.36% | 95.6% | 86.5% | 100.3%
Class C | 0.10% | 0.08% | -0.01% | 97.5% | 94.2% | 100.0%
Class E | 0.13% | 0.25% | 0.20% | 96.1% | 86.3% | 100.0%
Overall | 0.09% | 0.06% | 0.19% | 96.3% | 88.9% | 100.1%
Class D | -0.05% | 0.47% | 0.27% | 99.4% | 98.4% | 100.1%
Class F | -0.01% | 0.26% | -0.45% | 97.6% | 93.3% | 99.9%
Class TGM |  |  |  |  |  | 
QP-22 runtimes are 88.5% and 88.9% for RA and LDB configurations.

## Slide 6: Summary
This contribution proposes to modify the MTT early termination method defined in JVET-AF0111 by also considering the CABAC cost of coding the split mode.
Test1 shows QP-22 encoding time reduction of 9%, 14% and 13% for AI, RA and LDB configurations with limited degradation in coding efficiency.
Thanks to Nokia, Xiaomi and Tencent for cross-checking.

## Slide 7
Thanks