## Slide 1: Non-EE2: OBIC extension with PDP and advanced sampling strategy
Jiaye Fu (Peking Univ.) Kemer, 2024.11
Notes: Hi This is the proposal “Non-EE2: Improved OBIC with PDP” from PKU

## Slide 2: Introduction
OBIC in ECM-14.0:
  Derived intra modes according to the occurrence of the intra modes in the spatial neighborhood of the block
  Fusion-based Intra Prediction
Matrix-based Intra Prediction in ECM-14.0
  P(x,y) = ∑k F(x,y,k)*r(k), where r(k) denotes as reference pixel and F(x,y,k) is the matrix of weights
  Replacing Conventional Intra Angular Prediction
  Implemented in DIMD
Notes: # It uses polynomials and pre-set weights to make predictions about the current block

## Slide 3: Improved OBIC with PDP
Aspect #1: OBIC extension with PDP
  Intra Mode selected by OBIC can be either intra angular prediction mode or matrix-based intra prediction mode
Aspect #2: OBIC extension with advanced sampling strategy
  In this contribution, the 18 non-adjacent sampling points have been extended to 87 non-adjacent sampling points

## Slide 4: Results
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.02% | -0.09% | -0.11% | 100.9% | 98.0% | 99.7% | 100.0%
Class A2 | -0.01% | -0.11% | -0.02% | 103.0% | 101.7% | 100.5% | 100.0%
Class B | -0.02% | 0.06% | 0.09% | 102.3% | 102.5% | 99.9% | 100.1%
Class C | -0.01% | -0.07% | -0.07% | 101.8% | 102.1% | 100.5% | 100.0%
Class E | -0.03% | 0.03% | 0.24% | 102.4% | 100.5% | 97.8% | 99.9%
Overall | -0.02% | -0.03% | 0.03% | 102.1% | 101.2% | 99.7% | 100.0%
Class D | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!

## Slide 5: Conclusion
This contribution suggests the adoption of an advanced sampling strategy and the incorporation of PDP into OBIC as a way to align the methodology of DIMD and OBIC. The results show that the proposed method can improve the coding efficiency of ECM. It is suggested to further study this method in EE2.
Thanks to Transsion for cross-checking!

## Slide 6
Thank you