## Slide 1: JVET-AJ0276: Improvement to ALF scaling factor
Marta Karczewicz, Nan Hu, Hongtao Wang, Yiting Shao, Vadim Seregin (Qualcomm)

## Slide 2
ALF scaling factor in ECM-14.0
  Applied to correction residuals of ALF signalled filters
  A scaling factor is signalled for each ALF class
Proposal
  Two scaling factors can be signalled for each ALF class
    Controlled by a flag whether one or two scaling factors are signalled
    Samples are further classified based on boundary information
    One scaling factor for boundary samples and the other for non-boundary samples

## Slide 3: Results
JVET-AJ0276
JVET-AI0084 (Performance of scaling factor adopted in last meeting)
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.05% | -0.21% | -0.12% | 100.1% | 100.1% | 100.2% | 100.0%
Class A2 | -0.05% | -0.16% | 0.07% | 99.8% | 99.8% | 100.2% | 99.7%
Class B | -0.02% | -0.04% | -0.13% | 99.9% | 100.0% | 100.0% | 100.0%
Class C | -0.07% | -0.01% | -0.05% | 100.1% | 100.2% | 100.0% | 100.2%
Class E |  |  |  |  |  |  | 
Overall | -0.05% | -0.09% | -0.07% | 99.9% | 100.0% | 100.1% | 100.0%
Class D | -0.12% | -0.04% | -0.02% | 99.9% | 100.1% | 99.9% | 100.0%
Class F | -0.02% | 0.01% | 0.03% | 100.2% | 100.0% | 100.1% | 100.1%
Class TGM | -0.07% | 0.02% | 0.04% | 100.3% | 99.9% | 100.0% | 97.9%
Low delay B Main 10 |  |  |  |  |  | 
Over ECM-13.0 |  |  |  |  |  | 
Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
-0.11% | -0.60% | -0.01% | 99.8% | 100.0% | 100.0% | 100.2%
-0.12% | -0.14% | -0.40% | 100.1% | 99.9% | 100.0% | 100.0%
-0.17% | 0.60% | 0.14% | 100.2% | 99.8% | 100.4% | 100.3%
-0.13% | -0.15% | -0.10% | 100.0% | 99.9% | 100.1% | 100.1%
-0.23% | -1.14% | -0.67% | 100.2% | 99.5% | 100.6% | 100.0%
-0.21% | -0.08% | -0.78% | 100.0% | 100.8% | 100.4% | 99.9%
-0.19% | -0.05% | -0.14% | 99.9% | 100.0% | 100.0% | 95.5%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.02% | -0.14% | 0.02% | 99.5% | 100.1% | 100.0% | 100.3%
Class A2 | -0.03% | 0.13% | 0.04% | 99.9% | 100.1% | 100.4% | 100.9%
Class B | -0.05% | 0.12% | 0.09% | 100.1% | 100.0% | 100.1% | 100.5%
Class C | -0.11% | -0.02% | 0.06% | 99.7% | 99.4% | 100.2% | 100.5%
Class E |  |  |  |  |  |  | 
Overall | -0.06% | 0.03% | 0.06% | 99.8% | 99.9% | 100.2% | 100.5%
Class D | -0.06% | 0.20% | 0.00% | 100.5% | 100.2% | 100.1% | 100.2%
Class F | -0.03% | 0.07% | 0.16% | 100.3% | 100.3% | 100.0% | 97.1%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Low delay B Main 10 |  |  |  |  |  | 
Over ECM-14.0 |  |  |  |  |  | 
Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
0.00% | 0.28% | -0.09% | 99.5% | 99.8% | 99.4% | 101.4%
-0.10% | 0.44% | 0.21% | 99.9% | 100.1% | 100.3% | 100.0%
-0.09% | 0.30% | -0.38% | 100.0% | 99.7% | 98.4% | 99.9%
-0.06% | 0.34% | -0.06% | 99.8% | 99.9% | 99.4% | 100.5%
-0.06% | 0.18% | 0.48% | 100.2% | 99.9% | 99.6% | 100.1%
-0.17% | 0.29% | 0.05% | 99.8% | 99.5% | 100.2% | 100.7%
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!