| Joint Video Team (JVT) of ISO/IEC MPEG & ITU-T VCEG (ISO/IEC JTC1/SC29/WG11 and ITU-T SG16 Q.6) 15th Meeting: Busan, KR, 16-22 April, 2005 | Document VCEG-Z08 Filename: VCEG-z08.doc Generated: 5 April ’05 |
| --- | --- |

| Question: | Q.6/SG16 (VCEG) |
| --- | --- |
| Source: | Gisle Bjontegaard, Arild Fuldseth, Harald Dankworth Philip Pedersens vei 22 1366 Lysaker, Norway | Tel: Fax: Email: | +47 67125125 +47 67125234 gbj@tandberg.no afu@tandberg.no harald.dankworth@tandberg.net |
| Title: | Modified simple chroma interpolation filter |
| Purpose: | Proposal. |

_____________________________

# Background

VCEG-Y09 defines a simple chroma interpolation.  It reduces interpolation complexity.  Coding performance is changed little except for Mobile and Tempete (+5.5% and +3.3%).  The present document defines a modified interpolation that avoids the loss in coding gain and still maintain the complexity reduction.

The method is characterized by:

- Downscaling vectors to obtain chroma vectors in ¼ chroma pixel units

- Interpolation method similar to the simplified luma interpolation defined in VCEG-W09

# The method

## Downscaling

Vluma  is a luma vector component in ¼ luma pixel units.  Similarly Vchroma is a chroma vector component in ¼ chroma pixel units.  Vchroma is derived from Vluma :

Vchroma = (Vluma + offset)>>1      offset = 0 or 1 for every other picture.

## Interpolation

We now have chroma vectors in ¼ chroma pixel units and use a similar interpolation method to that proposed as simple luma interpolation in VCEG-W09 for ¼ pixel interpolation.

Capital letters (A, B, C, D) in the figure means integer chroma pixel positions, whereas lower case letters means fractional chroma pixel positions.

A     a     b     c     B

d     e     f     g     h

i     j     k     l     m

n     o     p     q     r

C     s     t     u     D

The fractional pixel values are defined as:

b = (A + B)>>1,   m = (B + C)>>1,   t = (C + D)>>1,   i = (A + C)>>1,   k = (C + B)>>1

a = (A + b + 1)>>1,	c = (B + b + 1)>>1,	d = (A + i + 1)>>1,	e = (b + i + 1)>>1

f = (A + m + 1)>>1,	g = (b + m + 1)>>1,	h = (B + m + 1)>>1,	j = (C + b + 1)>>1

l = (B + t + 1)>>1,	n = (C + i + 1)>>1,	o = (i + t + 1)>>1,	p = (D + i + 1)>>1

q = (m + t + 1)>>1,	r = (D + m + 1)>>1,	s = (C + t + 1)>>1,	u = (D + t + 1)>>1

# Simulation results

In VCEG-Y09 we reported bitrate changes and complexity reductions using the Tandberg encoder.  For direct comparisons we list the VCEG-Y09 results as well as the ones from the present document in the tables below.

| Sequence | Bitrate for simple chroma interpolation (%) |
| --- | --- |
|  | VCEG-Y09 | New proposal (VCEG-Z08) |
| Container | 0.07 | -0.18 |
| Foreman | 0.29 | 0.23 |
| News | 0.44 | 0.66 |
| Silent | 0.14 | -0.17 |
| Paris | 0.32 | 0.04 |
| Mobile | 5.50 | 0.28 |
| Tempete | 3.29 | 0.11 |
| Average | 1.44 | 0.14 |

| Sequence | Reduction of total number of cycles with the simplified chroma interpolation compared with H.264 at QP=32 (%) |
| --- | --- |
|  | VCEG-W09 | New proposal (VCEG-Z08) |
| Container | -2.4 | -3.29 |
| News | -1.6 | -3.40 |
| Foreman | -2.1 | -3.24 |
| Silent | -2.2 | -4.16 |
| Paris | -1.2 | -2.69 |
| Mobile |  | -2.83 |
| Tempete |  | -3.35 |

It is seen that the bitrate is practically unchanged using the new simple chroma interpolation.  At the same time the reduction in computer cycles is larger than in VCEG-W09.

In VCEG-Z10.xls there are more simulation results.  (Simple luma and chroma interpolation are linked together in the results in VCEG-Z10.xls).

# IPR statement

TANDBERG may have IPR connected to the proposed method and based on reciprocity TANDBERG is prepared to grant a license on reasonable and non discriminatory terms.