## Slide 1: VCEG-AZ05 Known tools performance investigation for next generation video coding
E.Alshina, A.Alshin, J.-H. Min, K. Choi,
A.Saxena, M. Budagavi (Samsung Electronics)

## Slide 2: HM-KTA tools summary
HEVC v1 | HM-KTA rc1 | Investigated tools
CU 16…64 | CU 16…64,128,256 | CU 16…256
TU 4…32 | TU 4…32, 64 | TU 4…64
INTRA: Planar+DC+33 Angular | INTRA: Planar+DC+33 Angular | INTRA: Planar+DC+65 Angular
 | LM-Chroma | LM-Chroma
DCT2 , DST7 (4x4) | DCT2, DCT5, DCT8, DST1, DST7 | DCT2, DCT5, DCT8, DST1, DST7
- | - | Adaptive secondary transform (ROT)
- | - | Multi-Parameter Intra (MPI)
- | - | Bi-directional optical flow
- | - | Multi-parameter CABAC probability up-date
- | Adaptive Loop Filter (ALF) | Adaptive Loop Filter (ALF)
TMVP | Advanced Temporal Motion Vector Prediction (ATMVP) | Advanced Temporal Motion Vector Prediction (ATMVP)
- | Overlapped Block Motion Compensation (OBMC) | Overlapped Block Motion Compensation (OBMC)
2013, Jan
2015, Feb
2015, June

## Slide 3: Test results summary
HM-14.0 | HM-KTArc1 |  |  |  |  | "+investigated tools" |  | 
 | All Intra Main |  |  |  |  | All Intra Main |  | 
 | Y | U | V |  |  | Y | U | V
Class A | -8,8% | -23,8% | -18,8% |  |  | -12,3% | -28,2% | -23,9%
Class B | -6,4% | -11,7% | -8,6% |  |  | -9,9% | -16,5% | -14,3%
Class C | -6,5% | -11,8% | -13,9% |  |  | -9,6% | -16,2% | -18,5%
Class D | -4,8% | -10,1% | -10,4% |  |  | -7,2% | -13,1% | -13,9%
Class E | -7,3% | -12,3% | -14,2% |  |  | -11,0% | -18,3% | -20,0%
Overall | -6,7% | -13,9% | -12,9% |  |  | -10,0% | -18,4% | -17,8%
Class F | -7,0% | -11,6% | -11,1% |  |  | -8,8% | -14,1% | -13,4%
 | Random Access Main |  |  |  |  | Random Access Main |  | 
 | Y | U | V |  |  | Y | U | V
Class A | -12,5% | -29,5% | -24,7% |  |  | -15,3% | -32,6% | -27,9%
Class B | -10,4% | -15,4% | -11,5% |  |  | -14,2% | -19,7% | -16,1%
Class C | -9,1% | -12,4% | -14,8% |  |  | -12,8% | -16,4% | -18,6%
Class D | -9,6% | -11,0% | -11,5% |  |  | -13,7% | -14,9% | -15,1%
Overall | -10,4% | -17,0% | -15,4% |  |  | -14,0% | -20,8% | -19,2%
Class F | -6,6% | -12,6% | -12,0% |  |  | -8,6% | -14,8% | -14,3%
 | Low delay B Main |  |  |  |  | Low delay B Main |  | 
 | Y | U | V |  |  | Y | U | V
Class B | -8,9% | -10,2% | -8,5% |  |  | -9,8% | -11,3% | -9,6%
Class C | -8,6% | -7,9% | -8,6% |  |  | -9,3% | -8,7% | -9,5%
Class D | -8,1% | -6,2% | -6,4% |  |  | -8,4% | -6,7% | -7,0%
Class E | -10,7% | -13,4% | -17,5% |  |  | -12,0% | -16,8% | -20,1%
Overall | -9,0% | -9,2% | -9,7% |  |  | -9,8% | -10,5% | -10,9%
Class F | -5,5% | -9,8% | -9,1% |  |  | -6,2% | -10,3% | -10,0%
 | Low delay P Main |  |  |  |  | Low delay P Main |  | 
 | Y | U | V |  |  | Y | U | V
Class B | -13,7% | -14,2% | -11,3% |  |  | -14,6% | -15,3% | -12,4%
Class C | -10,1% | -9,4% | -10,6% |  |  | -10,8% | -10,3% | -11,5%
Class D | -9,4% | -7,6% | -7,9% |  |  | -9,9% | -8,5% | -8,2%
Class E | -14,4% | -16,3% | -20,0% |  |  | -15,7% | -19,8% | -22,3%
Overall | -11,9% | -11,8% | -11,9% |  |  | -12,7% | -13,2% | -13,0%
Class F | -11,9% | -11,8% | -11,9% |  |  | -12,7% | -13,2% | -13,0%
  Highest additional gain was observed:
  ALL INTRA:
  BasketballDrive 4,8%
  Johny 4,4%
  RANDOM ACCESS:
  BQSquare 6,1%
  Traffic 5,0%
  LOW DELAY B:
  KristenAndSara 1,8%
  Johny 1,7%
  LOW DELAY P:
  KristenAndSara 1,4%
  Johny 1,3%

## Slide 4: Intra: Finer granularity arbitrary directional intra prediction
Straight-forward extension of HEVC Angular Prediction
  HEVC angles:
    {2, 5, 9, 13, 17, 21, 26, 32}* /64
  Finer angles:
    {1, 2, 3, 5, 7, 9, 11, 13, 15, 17, 19, 21, 23, 26, 29, 32} * /64
  Total: 65 angles + planar + DC
  Syntax
    3 MPMs + 6 bits
JCTVC-A124, Dresden, April, 2010

## Slide 5: Intra: Multi-Parameter Intra (MPI)
Multi-Parameter Intra (MPI) provides more natural prediction patterns
  Uses a 4-point filter for each pixel inside the predicted block
Syntax: up to 2 bits per CU for indexMPI coding
indexMPI |  |  |  | Effect
0 | 4 | 0 | 0 | No post-processing
1 | 2 | 1 | 1 | Smoothing left and above
2 | 2 | 2 | 0 | Smoothing with above boundary
3 | 2 | 0 | 2 | Smoothing with left boundary
JCTVC-A124, Dresden, April, 2010

## Slide 6: Inter: Bi-directional optical flow
Fine motion compensation within bi-predicted blocks:
JCTVC-C204, Guangzhou, October, 2010
Parameters are not signaled, but calculated on a fly
G(k)x, G(k)y – gradients of the Prediction from Reference k
vx, vy – fine motion refinement inside PU
Observed effect: encoder chooses larger sizes PUs

## Slide 7
Probability up-date using exponential smoothing
takes into account values of ~ W recently decoded bins
Here, – current probability, – updated
probability after y =MPS?1:0 decoded bin,
W – “window size
W19.69 (both in AVC and HEVC)
  Entropy: Multi-parameter probability up-date in CABAC
JCTVC-F254, Torino, July, 2011
Multi-hypothesis probability up-date combines precise (long window) and robust (short window) hypothesis for probability
W=256
W=16
Hint: During first 50 up-dates only “short window” hypothesis is used (for faster adaptation after entropy reset)

## Slide 8
Transform & Quantization flow-chart
1D ROT example
  partial information redistribution between coefficients for error minimization
  Let’s qBits = 1 and c0 = 5 c1=3
    If =0 (no ROT)
      c0 = 5, c1=3  q0 = 2, q1 = 1  c0 = 4, c  1 = 2 |c0 – c  0| = 1, |c1 – c  1| = 1
    If , S and S  : r0 = c0 + c1 ; r1 = c0 – c1 and c  0 = (r  0 + r  1 )/2, c  1 = (r  0 – r  1 )/2
      c0 = 5, c1=3  r0 = 8, r1=2q0 = 4, q1 = 1  r0 = 8, r  1 = 2  c0 = 5, c  1 = 3 |c0 – c  0| = 0, |c1 – c  1| = 0
Syntax
  indexROT is coded with 2 bits per CU (“0”  no ROT, “1”,”2”,”3”  different 2nd transforms
  Transform & Quantization: Adaptive Secondary Transform
JCTVC-E380, Geneva, March, 2011
invQuant
invROT
invTransform
fwdQuant
fwdROT
fwdTransform
c  r  q
q  r’  c’

## Slide 9: Incremental gain vs HM-KTArc1
Tested tool | All Intra | RA
Fine Gr. Intra | 0.4% | 0,1%
mCABAC | 0,8% | 0,6%
BIO | - | 2,1%
MPI | 1,3% | 0,6%
ROT | 1,2% | 0,6%
TOTAL | 3,5% | 4,0%
HEVC ctc