## Slide 1: Status of H.BWC (Presentation for joint meeting of VCEG with SC29/WG6 MPEG Audio 2024-11-06) Contact: Jonathan Pfaff (H.BWC AHG Chair)

## Slide 2: CfP for H.BWC
DICOM approached ITU-T VCEG with request for biomedical waveform coding (BWC)
CfP issued in April 2024
3 biomedical waveform types: ECG, EMG, EEG
Bit-rates ranging from high quality to lossless for medical applications
4 responses to CfP by Dolby, ETRI, Fraunhofer HHI, and Philips
ECG (2 channels): significant coding gains and difference between submissions with best results for HHI submission
EMG (4 channels): similar results by most submissions
EEG (23 channels): similar results by Dolby and HHI submission
Varying complexity among proposals

## Slide 3: Experimental results: Setup
Anchor: Extended HE-AAC as in VCEG-BU01
  MSE-based encoder optimization (exhale)
  Agreed on with WG-6 experts during Hannover meeting
Error measure: Mean squared error (PRD)
For each dataset: Averages of rates and distortions per CfP-working point

## Slide 4: Experimental results for ECG

## Slide 5: Experimental results for EMG

## Slide 6: Experimental results for EEG

## Slide 7: Test Model v1 for H.BWC
Based on CfP results: HHI and Dolby will merge technologies forming Test Model for BWC v1 (TM.BWC v1)
TM.BWC v1 is planned to be an output of the ongoing VCEG meeting with editing period Dec 20, 2024
Joint software for TM.BWC v1 will be produced by HHI and Dolby by Jan 6, 2025

## Slide 8: Technologies in Test Model v1 for H.BWC
Flexible block partitioning with all blocks being a power of 2 between 64 and 2048
Block- and sample-based prediction like block-matching prediction, inter-channel prediction, least mean squares prediction in transform domain
Scalar and trellis coded quantization
Lossless coding using integer lifting transform and bypass
Block-based transform
Entropy coding via VLC and arithmetic coding

## Slide 9: Next Steps for H.BWC
Communicate results of CfP including TM.BWC v1 and software with DICOM
Based on TM.BWC v1: experiments will be conducted starting at the Jan 2025 meeting by evaluating
  Tools in TM.BWC v1
  Tools from the other CfP submissions
Timeline beyond Jan 2025 at this moment foresees ITU-T approval by Oct 2025 – but this needs to be discussed further