ITU - Telecommunications Standardization Sector

STUDY GROUP 16

Video Coding Experts Group (Question 15)

_________________

Fourth Meeting: Tampere, Finland, 21-24 April, 1998

Document  Q15-D-44

Filename: q15d44.doc

Generated: 15 April ’98

| Question: | Q.15/SG16 |
| --- | --- |
| Source: | Torbjörn Einarsson and Per Thorell SCALAR ACTS project Ericsson Telecom Tellusborgsvägen 83 S-126 25 Stockholm Sweden | Tel: Fax: Email: | +46 8 681 3627 +46 8 719 0460 T.Einarsson@clab.ericsson.se |
| Title: | P-pictures in enhancement layers |
| Purpose: | Proposal for H.263++ |

_____________________________

Proposal

We propose that a new picture type, P-pictures in enhancement layers or EF-pictures, is included in H.263++ to provide a simple and efficient means for increasing the frame rate of enhancement layers.

The problem and the solution

Currently, the only way to increase the frame rate in an enhancement layer is to use B-pictures.

This has a number of disadvantages:

A delay is introduced because of out-of-order processing of pictures

Extra memory is needed for one or more frame storages

The implementation is rather complex

B-pictures cannot be used as reference for higher layers, which means that the bits spent on B-pictures are wasted for producing additional higher quality layers.

There is a simple solution to all of the above problems, which was unfortunately overseen when creating H.263+. That is to add the possibility of P-pictures in enhancement layers. Since an ordinary P-picture does not have a layer number, we prefer to call the new picture type EF (Enhancement Forward) picture.

Implementation of EF-pictures

An EF-picture has only forward prediction in contrast to an EP-picture that has both forward and upward prediction. All options that can be used for P-pictures can be used for EF-pictures.
However, since an EF-picture needs an ELNUM field, we suggest that it is signaled as a new picture type using, for example, Picture Type Code “110”.

Normally, an EF-picture would only need an ELNUM field, but it may also be useful to have an RLNUM field. For example, one could construct EF-pictures that are in a separate layer and thus disposable.

An example

The following example shows the implementation of three layers (QCIF,15Hz), (QCIF,30Hz), (CIF,30Hz) using B-pictures and EF-picture respectively. The advantages of the EF-picture approach is

Simple implementation

No extra delay because of out-of-order processing

No extra frame store is needed

The EF-picture is used as reference for Enhancement Layer 2.

Figure 1. Three layers with increasing frame rate using B-pictures

Figure 2. Three layers with increasing frame rate using EF-pictures