## Slide 1: Caller ID Spoofing, Egypt experience
Dr. Hosam Abd Elmaoula
NTRA
EGYPT
ITU Workshop on “Caller ID Spoofing”
(Geneva, Switzerland, 2 June 2014)

## Slide 2: Content
            Introduction
  Definition of Spoofing
  Types of Spoofing
  Potential Impacts of Spoofing in Egypt
            Methods of ID-Spoofing in Egypt
  Operator Procedures
    SIM box
    Re-file
  Consumer Procedures
    Call Back
    SIM Card
    Applications mobile / website
    OTT
            Combating ID-Spoofing in Egypt
            Recommendations

## Slide 3: Spoofing
            Spoofing is the act of one person pretending to be someone else

## Slide 4: Types of Spoofing
            Caller ID spoofing
            Is when a telephone's caller ID displays a number that does not belong to the person calling.
            IP Spoofing
            A technique used to gain unauthorized access to computers.
            URL Spoofing
            A website shows another website.
            E-mail Address Spoofing
            A message coms from any e-mail address the sender chooses.

## Slide 5: Impacts
            Inability to provide accuracy of charging, mutual settlements and accounting.
            Limiting the recipient ability to reject call attempts, which could have economic implications on the callee as well as the privacy.
            Inability to stop automated telemarketing calls.
            Callee deception, when he receives a call showing a local number, whereas the caller is outside of the callee country placed by international call.
            Impersonation, where a caller or message source can impersonate a known entity to the user by spoofing it’s number.
            Denial of services, route a huge number of calls to drop the services.

## Slide 6: Methods of ID Spoofing in Egypt Operator procedures
SIM BOX

## Slide 7: Methods of ID Spoofing in Egypt Operator procedures
            Re-file occurs when the traffic is sent to a hub and then routed through a gateway that appears to re-originate the calls, so that they are not filed as “transit” traffic under international settlements.

## Slide 8: Methods of ID Spoofing in Egypt Consumer procedures
Traditional Call Back
Step 1 – Registration
            Web Registration - enter account number, PIN and phone number in the web form sonatelco.com
            Mobile Registration - call the access number
Step 2 - Make Calls
            Dial one of the callback access numbers provided in your panel.
            Listen for at least 1 ring and hang up and wait for call back.
            Pick up the hand set on the callback and listen for a 'BEEP'.
            Enter in the destination number you wish to call follow by #. Example - 9654435676#

## Slide 9: Methods of ID Spoofing in Egypt Consumer procedures
            Advanced Call Back - SIM Card
            All what explained in the previous technique can be done by inserting a very slim SIM Card in the handset
By using a SIM card you can make a call to anyone and hide or change your caller ID.

## Slide 10: Methods of ID Spoofing in Egypt Consumer procedures
Applications Mobile / Website
( ex. one leg call)
Group spoofing
Disguise your number
Change your voice
Add background noise
http://www.spoofcard.com/?utm_source=pj&utm_medium=Affiliate&source=pjn&subid=7504

## Slide 11: Methods of ID Spoofing in Egypt Consumer procedures
Over The Top (OTT)

## Slide 12: Fighting ID-Spoofing in Egypt SIM BOX
Via Mobile
Test Call Generation (TCG)
Profiling
Group Killing
MSRN
TGT

## Slide 13: Fighting ID-Spoofing in Egypt SIM BOX
Via Internet
Internet VoIP Filter (Operator Level /Country Level)
Detect and Stop/Throttle Bypassing IPs .

## Slide 14: Fighting ID-Spoofing in Egypt
Re-file
Fighting RE-file by modifying the commercial deals with carriers.
Call Back and SIM card
Fighting Call Back and SIM card by blocking the ranges of the numbers and IPs.
OTT services
Fighting the implications of OTT services by regulations including well defined SLA.

## Slide 15: Proposed Actions
To conduct studies to characterize possible types and ways of illegal ID spoofing.
To develop Recommendations on regulatory measures to assist MSs and Operating Agencies to combat ID spoofing.
To develop guides and bet practices, taking into account case studies from different regions of the world.

## Slide 16
Thank You