## Slide 1: A global Service layer platform for M2M communications
Dr. Friedbert Berens
FBConsulting Sarl, Luxembourg
friedbert.berens@me.com
ITU Workshop on the “Internet of Things -
Trend and Challenges in Standardization”
(Geneva, Switzerland, 18 February 2014)

## Slide 2: Mission
oneM2M is working to unify the Global M2M Community, by enabling the federation and interoperability of M2M systems, across multiple networks and topologies.

## Slide 3: Global Partners

## Slide 4: Scope & Objectives
To develop: Global M2M end-to-end specifications - using common use cases and architecture principles across multiple M2M applications to connect M2M devices with application servers worldwide with an access independent view of end-to-end services
To define: Service Layer platform with high level / detailed service architecture including: - Protocols/APIs/standard objects (open interfaces & protocols) - Interoperability, test and conformance specifications - Common use cases, terminal/module aspects - Service Layer interfaces/APIs between:
  Application and Service Layers
  Service Layer and communication functions
  Security and privacy aspects
  authentication, encryption, integrity verification

## Slide 5: M2M Service Layer
Middleware - supporting secure end-to-end data/control exchange between M2M devices and customer applications by providing functions for remote provisioning & activation, authentication, encryption, connectivity setup, buffering, synchronization, aggregation and device management
  - software layer
  - sits between M2M applications and communication elements that provides data transport
  - normally rides on top of IP
  - provides commonly needed functions for M2M applications across different industry segments

## Slide 6: Vision:
Interconnecting the Internet of Things; Connecting the Un-connected
Underlying protocols
oneM2M
Other M2M protocol
Hybrid protocol App
oneM2M protocol
Other M2M protocol
App
oneM2M native App
Underlying protocol
Underlying protocol
IoT Device
IoT Device

## Slide 7: Horizontal Platform Vision
Local NW
Pipe (vertical):
1 Application, 1 NW, 1 (or few) type of Device
Business Application
Device
Communication Network (mobile, fixed, Powerline ..)
Gateway
Horizontal (based on common Layer)
Applications share common infrastructure, environments and network elements
Communication Network 1
Communication Network 2
Local NW
Device
Device
Device
Device
Common Application Infrastructure/Service layer
Gateway
IP
Business Application #1
Business Application #2
Business Application #n

## Slide 8: oneM2M simplified Architecture
AE
AE
AE
CSE
CSE
CSE
M2M Applications
M2M Service layer
Underlying Transport
Mca
Mca
Mca
Mcc
Mcc
Mcn
Mcn
Mcn
Mcn
NSE
NSE
Network Service Entity

## Slide 9: oneM2M Common Service Functions
Ref: oneM2M TS: Functional Architecture

## Slide 10: OneM2M architecture entities
AE: Application Entity, containing the application logic of the M2M solution like home management functions, fleet management, blood sugar monitoring
CSE: Common Service Entity containing a set of common service functions (CFE) that are common to a broad range of M2M environment (verticals). This is the main part of the oneM2M specification
CSF: Common Service Functions included in a CSE, CSFs can be mandatory or optional, CSF can contain sub-functions (mandatory or optional)
NSE: Network Service Entity, provides network services to the CSE, like device triggering, device management support, location services. These services are related to the underlying network capabilities

## Slide 11: OneM2M architecture Reference points
Mca- Reference Points: the interface point between the AE and the CSE, the Mca point provides the M2M applications access to the common services included in the CSE. The AE and CSE my be co-located in the same physical entity or not
Mcc- Reference Points: This is the reference point between two CSEs. The Mcc reference point shall allow a CSE to use the services of another CSE in order to fulfil needed functionality. Accordingly, the Mcc reference point between two CSEs shall be supported over different M2M physical entities. The services offered via the Mcc reference point are dependent on the functionality supported by the CSEs
Mcn- Reference Points: This is the reference point between a CSE and the Underlying Network Services Entity. The Mcn reference point shall allow a CSE to use the services (other than transport and connectivity services) provided by the Underlying Network Services Entity in order to fulfil the needed functionality.
Mcc‘- Reference Point: interface between two M2M service providers, As similar as possible to the Mcc reference point. But due to the nature of inter-M2M Service Provider communications, some differences are anticipated.

## Slide 12: oneM2M Organization
Steering Committee (Partners)
Technical Plenary (Members / Partners)
Protocols WG3
Requirements WG1
Architecture WG2
Security WG4
Management, Abstraction, Semantics WG5
Legal
Methods & Processes
Method of Work
Finance
MARCOM
Work Programme

## Slide 13: Work Areas
WG1 - Requirements
  Input accepted on more than 100 service requirements
WG2 - Architecture
  Distilling service-layer architectural options
WG3 - Protocols
  Assessing protocols for service layer, and interoperability
WG4 - Security
  Ensuring Security and Privacy aspects are considered
WG5 - Management & Semantics
  Providing device management; Working on semantic library

## Slide 14: Schedule towards Release 1
Requirements
Architecture
Protocols
Security
Management, Abstraction, Semantics
Target Date: Release 1

## Slide 15: Participation
Levels of participation:
  Partner Type 1
    Member companies participate directly
  Partner Type 2
    Contributes on behalf of Member companies
  Associate Member
  Join: http://www.onem2m.org/join.cfm
  Docs: http://www.onem2m.org/library/index.cfm
  News: http://www.onem2m.org/subscribe.cfm

## Slide 16: www.oneM2M.org