## Slide 1: 31ST ITU-T Quality of Service Development Group (QSDG) Meeting
Eng. John S. Kimbe
SATA Secretariat
4th – 6th November 2014
Sheraton Jumeira Beach Resort
Dubai, United Arab Emirates
Reliability and Availability

## Slide 2: 1. Definition
Reliability can be defined as “the probability that an item will perform its intended functions for a specified interval under stated conditions”. It can be measured by Mean Time Between Failures (MTBF) and predicted Reliability (R) = e-?t, where t is the time in service.
Availability can be defined as “the probability that an item is in an operable state” and is generally calculated as MTBF/(MTBF+MDT) where MDT = mean downtime also

## Slide 3: 2. Reliability
The term reliability refers to the ability of a computer-related hardware or software component to consistently perform according to its specifications. In theory, a reliable product is totally free of technical errors. In practice, vendors commonly express product reliability as a percentage. The Institute of Electrical and Electronics Engineers ( IEEE ) sponsors an organization devoted to reliability in engineering known as the IEEE Reliability Society (IEEE RS).

## Slide 4: 3. Availability
Availability is the ratio of time a system or component is functional to the total time it is required or expected to function. This can be expressed as a direct proportion (for example, 9/10 or 0.9) or as a percentage (for example, 90%). It can also be expressed in terms of average downtime per week, month or year or as total downtime for a given week, month or year. Sometimes availability is expressed in qualitative terms, indicating the extent to which a system can continue to work when a significant component or set of components goes down.

## Slide 5: 4. Serviceability
Serviceability is an expression of the ease with which a component, device or system can be maintained and repaired. Early detection of potential problems is critical in this respect.
Some systems have the ability to correct problems automatically before serious trouble occurs; examples include built-in features of OSs such as Microsoft Windows XP and auto-protect-enabled anti-virus software and spyware detection and removal programs. Ideally, maintenance and repair operations should cause as little downtime or disruption as possible.

## Slide 7: 5. Key Elements of RAS
Some of the key elements of RAS are:
Over-engineering, which is designing systems to specifications better than minimum requirements.
Duplication, which is extensive use of redundant systems and components.
Recoverability, which is the use of fault-tolerant engineering methods.
Automatic updating, which keeps OSs and applications current without user intervention.
Data backup, which prevents catastrophic loss of critical information.

## Slide 8: 6. Key Elements of RAS
Data archiving, which keeps extensive records of data in case of audits or other recovery needs.
Power-on replacement, which is the ability to hot swap components or peripherals.
The use of virtual machines, which minimizes the impact of OS or software faults.
Use of surge suppressors, which minimizes risk of component damage resulting from power-line anomalies.
Continuous power, which is the use of an Uninterruptible Power Supply (UPS) keeps systems operational while switching from commercial power to backup or auxiliary power.
Backup power sources, which includes batteries and generators to keep systems operational during extended interruptions in commercial power.

## Slide 9: 7. Hardware Failures
Hardware failures are typically characterized by a bath tub curve.
The chance of a hardware failure is high during the initial life of the module.
The failure rate during the rated useful life of the product is fairly low.
Once the end of the life is reached, failure rate of modules increases again.

## Slide 11: 8. Hardware Failure Attributes
Design failures: This class of failures take place due to inherent design flaws in the system. In a well-designed system this class of failures should make a very small contribution to the total number of failures.
Infant Mortality: This class of failures cause newly manufactured hardware to fail. This type of failures can be attributed to manufacturing problems like poor soldering, leaking capacitor etc. These failures should not be present in systems leaving the factory as these faults will show up in factory system burn in tests.
Random Failures: Random failures can occur during the entire life of a hardware module. These failures can lead to system failures. Redundancy is provided to recover from this class of failures.
Wear Out: Once a hardware module has reached the end of its useful life, degradation of component characteristics will cause hardware modules to fail. This type of faults can be weeded out by preventive maintenance and routing of hardware.

## Slide 13: 9. Software Failures
Software failures can be characterized by keeping track of software defect density in the system. This number can be obtained by keeping track of historical software defect history. Defect density will depend on the following factors:
Software process used to develop the design and code (use of peer level design/code reviews, unit testing)
Complexity of the software
Size of the software
Experience of the team developing the software
Percentage of code reused from a previous stable project
Rigor and depth of testing before product is shipped.
Defect density is typically measured in number of defects per thousand lines of code (defects/KLOC).

## Slide 14: Downtime per year is a more intuitive way of understanding the availability. The table below compares the availability and the corresponding downtime.
Availability | Downtime
90% (1-nine) | 36.5 days/year
99% (2-nines) | 3.65 days/year
99.9% (3-nines) | 8.76 hours/year
99.99% (4-nines) | 52 minutes/year
99.999% (5-nines) | 5 minutes/year
99.9999% (6-nines) | 31 seconds/year !